## Slide 1: Ritvik Narula
August 2026
Georgia Tech | Computer Engineering

## Slide 2: The problem
Validating an automotive ECM means reading its signals on an oscilloscope - by hand.
Slow & manual
- An engineer reads the scope for every test
- The automated sequence stops and waits for a person
Not repeatable
- Readings are subjective, hard to reproduce
- Can't be regressed across ECM software builds
Not traceable
- No automatic record tying result to requirement
- Hard to prove coverage for audits (ASPICE)
The bottleneck: a human in the middle of an otherwise automated test.

## Slide 3: What, why, how
WHAT
Automate the instruments
- Software that drives the oscilloscope and function generator directly
- One consistent way to set up, capture and measure
WHY
Take the person out of the loop
- Faster, repeatable, objective results
- Frees engineers from watching a screen
HOW
Plug into the existing test system
- Slots into TestStand as ordinary Python steps
- Reuses the bench already on the floor - no new hardware
The result: a hands-off measurement block the whole team can rely on.

## Slide 4: Where the code sits
THE USUAL WAY VS. THIS PROJECT
Typical setup (VISA)
TestStand / Python
|
PyVISA
wrapper library
|
NI-VISA driver
install + license
|
Instrument
4 layers - an extra driver to install
This project (direct)
TestStand / Python
|
Raw network socket (SCPI)
just a message
|
Instrument
3 layers - nothing extra to install
vs
Why it matters: one fewer layer to install, license and debug on every bench - the code talks to the instrument as plainly as sending a text message.

## Slide 5: How it fits on the bench
HIL Bench - TestStand
orchestrates the whole test, hands-off
Function Generator
creates the input signal
ECM
the unit under test
Oscilloscope
captures the response
>
stimulus
>
response
controls all three over the network (SCPI)
The bench runs the ECM, the generator drives it, the scope watches - and the HIL bench commands every piece. No manual step in between.

## Slide 6: The building blocks
A small, plain-English set of calls - the same shape for every instrument.
Set up & drive
connect(...)
Find the instrument and open a session
configure(...)
Apply a saved setup; verify every setting
generate / output_on(...)
Drive a known signal into the ECM
arm(...)
Get ready to catch a one-time event
Capture & measure
capture(...)
Read the waveform into memory
rms / frequency / delay(...)
Pull the number the test needs
save_png / save_csv(...)
Store the evidence, auto-labeled
Each call takes a name and plain numbers - readable by anyone, not just the author.

## Slide 7: One clean sequence, end to end
1
Connect
find + open
>
2
Configure
apply setup
>
3
Arm
ready to catch
>
4
Generate
drive signal
>
5
Capture
read waveform
>
6
Save
png + csv
The same six steps run every test - from connecting to the bench to saving the labeled result.
Once the sequence starts, it runs to a saved, traceable result on its own.

## Slide 8: Results
Captured & measured automatically
Timing + levels, saved as evidence
Why it wins
- TestStand no longer pauses for a person to read the scope
- The sequence is hands-off - end to end automated
- Every result is captured, measured and saved the same way
The payoff: what used to be an engineer watching a screen mid-test is now a step that runs itself - saving time on every run and making the whole sequence unattended and repeatable.

## Slide 9: Thank You